## Slide 1
Software Defined Networking Security
Chong Yu, Sovatha Sang, Damien Piris , Marc Suda, John Jay College of Criminal Justice, Manhattan, NY 10019
Sven Dietrich, Associate Professor, Mathematics and Computer Science Department John Jay College of Criminal Justice, Manhattan, NY 10019
Libpcap is a portable C/C++ library for network traffic packet capturing. Libpcap addresses these concerns by providing a common high-level application programming interface (API) into the packet-capturing frame-work of many operating systems (OS). Network analysis revolves around the Ethernet data-link layer. Packet capture is to get access to the underlying facility provided by the operating system so the program can grab packets in their raw form. The ether card picks up a packet from the network. Once the packet is handed off to the OS, the OS must determine what type of packet it is, to do so it strips off the Ethernet header of the packet and looks at the next layer. If it is an IP packet, the OS must now strip off the IP header and determine which type of IP packet it is. If the packet is determined a UDP packet, the UDP header is stripped off and the packet payload is handed over to the application that the packet is sent for. Packet capture allows us to intercept any packet that is seen by the network device.
Packet analysis, also referred to as packet sniffing or protocol analysis is an ever evolving algorithmic function. The network complications all start within the core of the packets. Because of this, packet sniffing is a useful tool to understand the information traveling through a network. Packet sniffing is used to better understand the data flow within a network. By mapping out the flow of the network, it could possibly close the case on where bottlenecks are present and how to increase network efficiency. Packet sniffing can also be used as diagnostic process for troubleshooting problems and solving them quickly and cost-effectively. This can be done by testing the network to see if information can get through an interface and ensure that firewalls, routers and switches are all working correctly. Packet sniffing is essentially a network intrusion detection system, discovering faulty networking hardware, and for educational purposes.
Packet Sniffer
In a month from now, there will be over 50 billion devices connected to the internet because of this our network will need to be scaled at a much larger rate.
SDN grants the ability to manage a network from a centralized perspective.
SDN virtualizes both the data and control planes allowing the user to provision physical and virtual elements from one location.
SDN gives the user more scalability providing the ability to provision resources at will you can change your network infrastructure at a moment’s notice.
SDN ENVIRONMENT
Advantages of SDN
Future work
Acknowledgements
References
This material is based upon work supported in part by the SUCCESS (Secure Communication and Computer Systems) Lab at TAMU. We thank Professor Dietrich for his guidance and motivation for our research and we also thank Professor Gu for his assistance with the Forenguard Tool, and Haopei Wang for the comments that greatly improved the implementation and understanding the concept of how Forenguard works with ODL Controller.
Try to install malicious applications on the SDN controller to gain control of the network.
Find ways to defend against incoming attacks (ex: using DELTA).
M. Dacier, H. Konig, R. Cwalinski, F. Kargl and S. Dietrich, "Security Challenges and Opportunities of Software-Defined Networking", IEEE Security & Privacy, vol. 15, no. 2, pp. 96-100, 2017. Available: 10.1109/msp.2017.46
J. Cao, Q. Li, R. Xie, H. Sun, G. Gu, M. Xu, and Y. Yang, “The CrossPath Attack: Disrupting the SDN Control Channel via Shared Links”
H. Wang, G. Yang, p, Chinprutthiwong, L. Xu, Y. Zhang, and G. Gu, “Towards Fine-grained Network Security Forensics and Diagnosis in the SDN Era”, 2018 ACM SIGSAC Conference on Computer and Communications Security (CCS ’18), Available: 10.1145/3243734.3243749
S. M. Mousavi and M. St-Hilaire, “Early detection of DDoS attacks against SDN controllers,” 2015 International Conference on Computing, Networking and Communications (ICNC), 2015. Available: 10.1109/iccnc.2015.7069319
Forenguard
Environment Setup
Implementation
Setup the environment using OpenDayLight SDN Controller
Start mongodb to collect and store data from mininet
Create a three-switch topology using mininet and openflow protocol
Prepare for the MAC spoofing attack within node H1,H2, and H3
Check all three hosts network configuration
H2 is spoofing H3’s MAC address then pings to H1
At the same time, H3 cannot make the connection with H1 anymore
ForenGuard is able to diagnose why H3 lost connection with H1.
By checking the diagnosis results, there are four events that are the root causes which are triggered by H2’s spoofing.
What is SDN? Software Defined Networking is an modern computer network architecture which defines how a networking and computing system can be built using a combination of open, software-based technologies and commodity networking hardware that separate the SDN control plane and the SDN data plane of the networking stack.
Before SDN/Traditional Networking? In traditional networking, the switch does not have programmability, the rules cannot be changed dynamically. In SDN, the switch is connected to a controller, which controls the actions of the switch. The controller can be programmed dynamically to control the switch.
Introduction
Project Setup:
OS: #57-Ubuntu SMP
Processor: 1.6 GHz Intel Core i5
Memory: 8 GB 1867 MHz DDR3
Tools used: ForenGuard
MongoDB
ODL Controller
OFSwitchBase DPID[00:00:00:00:00:00:00:02]:
-> Receive Event OFPacketInVer13
-> Init Function processPacketInMessage
-> Init Function addToPortMap
-> Write Variable macVlanToSwitchPortMap -254649434
-> Return Function addToPortMap
-> Init Function getFromPortMap
-> Read Variable macVlanToSwitchPortMap -517582621
-> Return Function getFromPortMap
-> Init Function pushPacket
-> Return Function pushPacket
-> Init Function writeFlowMod
-> send Message FLOW_MOD
-> Return Function writeFlowMod
-> Init Function writeFlowMod
-> send Message FLOW_MOD
-> Return Function writeFlowMod
-> Return Function processPacketInMessage
-> Return Function receive
OFSwitchBase DPID[00:00:00:00:00:00:00:02]:
-> Receive Event OFPacketInVer13
-> Init Function processPacketInMessage
-> Init Function addToPortMap
-> Write Variable macVlanToSwitchPortMap -517582621
-> Return Function addToPortMap
-> Init Function getFromPortMap
-> Read Variable macVlanToSwitchPortMap null
-> Return Function getFromPortMap
-> Init Function writePacketOutForPacketIn
-> Return Function writePacketOutForPacketIn
-> Return Function processPacketInMessage
-> Return Function receive
OFSwitchBase DPID[00:00:00:00:00:00:00:01]:
-> Receive Event OFPacketInVer13
-> Init Function processPacketInMessage
-> Init Function addToPortMap
-> Write Variable macVlanToSwitchPortMap -517582622
-> Return Function addToPortMap
-> Init Function getFromPortMap
-> Read Variable macVlanToSwitchPortMap -254649433
-> Return Function getFromPortMap
-> Init Function pushPacket
-> Return Function pushPacket
-> Init Function writeFlowMod
-> send Message FLOW_MOD
-> Return Function writeFlowMod
-> Init Function writeFlowMod
-> send Message FLOW_MOD
-> Return Function writeFlowMod
-> Return Function processPacketInMessage
-> Return Function receive
OFSwitchBase DPID[00:00:00:00:00:00:00:01]:
-> Receive Event OFPacketInVer13
-> Init Function processPacketInMessage
-> Init Function addToPortMap
-> Write Variable macVlanToSwitchPortMap -254649433
-> Return Function addToPortMap
-> Init Function getFromPortMap
-> Read Variable macVlanToSwitchPortMap null
-> Return Function getFromPortMap
-> Init Function writePacketOutForPacketIn
-> Return Function writePacketOutForPacketIn
-> Return Function processPacketInMessage
-> Return Function receive
Cisco Systems Inc.
IBM Corporation
Hewlett Packard Enterprise
VMware
Juniper Networks
Huawei Technologies Co. Ltd.
Leading SDN Market Players:
Disadvantages of SDN
Increased complexity which allows hackers to control network operations in arbitrary ways, confuse or blind the defenders, and create inconsistencies
Inability to directly manage individual devices, leading to increased maintenance.
Increased latency due to infrastructure being virtualized.